## Slide 1: (Revised) Universal Soil Loss Equation (RUSLE)
An empirical model for estimating soil erosion

## Slide 2: Aims
Background
Factors controlling soil erosion
The RUSLE model for approximating soil loss rates
Implementing RUSLE model in a programming language

## Slide 3: Soil Erosion
The transport of soil particles from one location to another
Occurs naturally but is often made worse by management
  Average soil loss rates Europe: 17 t ha-1
  Average soil loss rates Natural Forest: 0.004-0.05 t ha-1 *
Soil erosion greater than rates of paedogenesis => will run out of well-developed soil
Nutrient loss/pollution (P), siltation of rivers
Dust Bowl, Texas, 1936 (Arthur Rothstein/Wikipedia)
*https://doi.org/10.1126/science.267.5201.1117

## Slide 4: Main RUSLE equation
Mean annual soil loss [t (ha year)-1]
Rainfall and runoff [MJ mm ha-1 year-1 hour-1 ]
Soil erodibility factor [t hour MJ-1 mm-1]
Slope length factor [-]
Slope steepness factor [-]
Cover and management factor [-]
Support practice factor [-]
Does not account for soil loss from landslides or soil loss from gullies
https://doi.org/10.5194/hess-22-6059-2018

## Slide 5: R – Rainfall and Runoff Factor
Captures the amount of rain and kinetic energy of a storm the soil is exposed to.
Can be thought of as kinetic energy per ha per year TIMES the maximum rainfall per hour the soils is exposed to () over 30 minutes:
= ‘storm kinetic energy’, = ‘maximum 30 minute rainfall intensity ’
is then the sum of monthly erosive storm () values occurring during a mean year:

## Slide 6: Computing
Measuring requires fancy equipment and storm conditions that often isn’t available
There are a number of studies which derive empirical relationships to quantify based on rainfall data only

## Slide 7: Computing
They worked out for the Algarve:
  Where is the monthly rainfall for days with >= 10mm of rain and is the monthly number of days with rainfall >=10mm of rain. This approximates with an They exclude months with no rainfall during calculation.
To calculate the average yearly :
And R has units MJ mm ha-1 year-1 hour-1

## Slide 8: Be careful, our apporximation is empirical
Is a function from a months rainfall to the real numbers:
It should always be positive, but is it? Think of a counter example
[0 0 0 0 10 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0]
Is it linear?
  Can we change the period or resolution?
Notes: A function is linear if and only if :
A function 𝑓:𝑅^𝑛→𝑅 is linear if and only if :
  𝑓(𝒙+𝒚)=𝑓(𝒙)+𝑓(𝒚) 𝑓𝑜𝑟 𝑎𝑙𝑙 𝒙,𝒚∈ℝ^𝑛
  𝑓(𝜆𝒙)=𝜆𝑓(𝒙) 𝑓𝑜𝑟 𝑎𝑙𝑙 𝒙∈ℝ^𝒏 𝑎𝑛𝑑 𝜆∈ℝ

## Slide 9: Jupyter NOTEBOOK: Section 𝑅 - Rainfall and Runoff Factor

## Slide 10: Main RUSLE equation
Mean annual soil loss [t (ha year)-1]
Rainfall and runoff [MJ mm ha-1 year-1 hour-1 ]
Soil erodibility factor [t hour MJ-1 mm-1]
Slope length factor [-]
Slope steepness factor [-]
Cover and management factor [-]
Support practice factor [-]
https://doi.org/10.5194/hess-22-6059-2018

## Slide 11: Soil erodibility factor -
Captures the influence of soil properties (e.g. soil texture, OM% etc) on susceptibility to erosion:
  “mean annual soil loss per unit of rainfall erosivity for a standard condition of bare soil, recently tilled up-and-down slope with no conservation practice at a 9% slope of length 22m”
100
1 unit of
m of tilled soil
9
How many tons of soil is lost from a ha in a year

## Slide 12: Soil erodibility factor -
From: https://doi.org/10.5194/hess-22-6059-2018
These are in imperial units, multiply by 0.1317 to convert to metric i.e.

## Slide 13: Soil erodibility factor -
From: https://doi.org/10.5194/hess-22-6059-2018
These are in imperial units, multiply by 0.1317 to convert to metric i.e.

## Slide 14: Analysis of equation for -
Where is the pH of the soil, is the % OM of soil, is sand %, , , is clay % and is silt %.
When pH increases K increases
When OM increases K decreases
When Sa increases K increases
When Cl increases K decreases
When Si increases K increases
Like for our equation for , when does this approximation break down?

## Slide 15: Jupyter NOTEBOOK: Section K - Soil erodibility factor

## Slide 16: Main RUSLE equation
Mean annual soil loss [t (ha year)-1]
Rainfall and runoff [MJ mm ha-1 year-1 hour-1 ]
Soil erodibility factor [t hour MJ-1 mm-1]
Slope length factor [-]
Slope steepness factor [-]
Cover and management factor [-]
Support practice factor [-]
https://doi.org/10.5194/hess-22-6059-2018

## Slide 17: Slope length and steepness factor-
Without this factor the equation would only be relevant to slopes of 9% with 22m length
and factors are used to adjust the erosion rates based on the slope angle and length of interest
There are several empirical equations for in the literature..

## Slide 18: Slope length and steepness factor-
From: https://doi.org/10.5194/hess-22-6059-2018

## Slide 19: Slope length and steepness factor-

## Slide 20: Jupyter Notebook: Section - slope length and steepness factor

## Slide 21: Main RUSLE equation
Mean annual soil loss [t (ha year)-1]
Rainfall and runoff [MJ mm ha-1 year-1 hour-1 ]
Soil erodibility factor [t h MJ-1 mm-1]
Slope length factor [-]
Slope steepness factor [t h MJ-1 mm-1]
Cover and management factor [-]
Support practice factor [-]
https://doi.org/10.5194/hess-22-6059-2018

## Slide 22: Cover and management factor -
Without the factor the equation would only be relevant to tilled soils. is defined as
  “the ratio of soil loss from a field with a given cover and management to that of a tilled fallow field”
  can be calculated based on satellite Normalized Difference Vegetation Index (NDVI, ‘greenness’) measurements
  Or values for similar management/cover areas in the literature can be used. See tables 8,9 10 in https://doi.org/10.5194/hess-22-6059-2018 or beyond. Choose ones relevant to your sites!

## Slide 23: Support practice factor
The factor is designed to capture the impact of conversation practices and is defined as:
  “The ratio of soil loss under a specific conservation practice to that of a field with tilled field”
  Factors can be taken from the literature to investigate how land owners can reduce soil erosion
https://doi.org/10.5194/hess-22-6059-2018

## Slide 24: Calcultaing
Jupyter Notebook: Section – putting it all together